## Slide 1
Wollo University
Kombolcha Institute of Technology
Department of Information System
Data Communication and Computer Networks

## Slide 2: Chapter 06: 6.0 Switching and Multiplexing
5.1 Switching Concept and Types
A network is a set of connected device.
Whenever we have multiple devices, we have the problem of how to connect them to make one to one communication possible.
One possible solution is to make a point to point connection between each pair of devices or between a central device and every other device.
These methods however are impractical and wasteful when applied to a very large networks.
The number and length of links require too much infrastructure to be cost efficient, the majority of those links would be idle most of the time.

## Slide 3: Cont…
A better solution is switching.
A switch network consists of a series of interlinked nodes called switches.
Switches are devices capable of creating temporary connections between two or more devices linked to the switch.

## Slide 4: Cont…
Traditionally there are three methods of switching
  Circuit switching
  Packet switching and
  Message switching
1. Circuit Switched Networks
A circuit switched network consists a set of switched connected by physical links.
A connection between the two stations is a dedicated path made of one or more links.
However, each connection uses only one dedicated channel in each link.
Each link is normally divided into n channels by using FDM or TDM.

## Slide 5: Cont… …
Circuit switching takes place at the physical layer
The actual communication in circuit switch network required three phases:
Connection setup,
Data transfer , and
Connection teardown.

## Slide 6: Cont…
Setup Phase
Before the two parties or multiple parties can communicate , a dedicated circuit needs to be established.
The end systems are normally connected through dedicated lines to the switches, so connection set up means creating a dedicated channel.
Data transfer phase
After the establishment of the dedicated circuit(channel), the two parties can transfer data.
Teardown Phase
When one of the parties needs to disconnect, a signal is sent to each switch to release the resources.

## Slide 7: Cont…
Efficiency
Circuit switch network is not as efficient as the other two types of network because resources are allocated during the entire duration of the connection
These resources are unavailable to other connections
Allowing resources to be dedicated means that other connections are deprived
Delay
Although circuit switched network normally has low efficiency, the delay in this type of network is minimal.

## Slide 8: Cont…
During data transfer the data aren’t delayed at each switch; the resources are allocated for the duration of the connection.
There is no waiting time at each switch.
The total delay is due to the time needed to create the connection , transfer data, and disconnect the circuit.

## Slide 9
2. Packet Switch Network
In data communication, we need to send messages from one end system to another.
If the message is going to pass through a packet switched network, it needs to be divided into packets of fixed or variable size.
The size of the packet is determined by the network and the governing protocols.
In packet switching,
    There is no resource allocation for a packet
    There is no reserved bandwidth on the links, and
    There is no scheduled processing time for each packet.
  Resources are allocated on demand

## Slide 10
The allocation is done on the first come first served basis.
The packet switch networks are sometimes referred to as connectionless network
The term connectionless here means that the switch (packet switch) doesn’t keep information about the connection state
There is no setup or teardown phases
Each packet is treated the same by a switch regardless of its source or destination

## Slide 11: Cont…
Routing Table
If there are no setup or tear down phases, the packets are routed to their destination by the routing table at the Switch or router.
The destination address and the corresponding forwarding output ports are recorded in the routing tables
Efficiency
The efficiency of packet switch network is better than that of circuit switched network; resources are allocated only when there are packets to be transferred.
Delay
There may be greater delay in packet switch network that the circuit switch network
Although there are no setup and teardown phase, each packet may experience a wait at a switch before it is forwarded

## Slide 12: Cont…
Message switching
Message (block data) is stored in a switching node and then forwarded later one hop at a time
Message received in its entirety , inspected for error, and then forwarded
Need “LARGE” storage space to store data in each node
Ex. Telegraph, military applications

## Slide 13: 6.2 Multiplexing Concepts and Types
Multiplexing is the name given to techniques, which allow more than one message to be transferred via the same communication channel.
The channel in this context could be a transmission line, e.g. a twisted pair or co-axial cable, a radio system or a fibre optic system etc.
The technique of transmitting multiple signals over a single medium is multiplexing.
Multiplexing is the transmission of multiple signals on one medium.
A channel is an assigned set of frequencies that is used to transmit the user’s signal
A channel will offer a specified bandwidth, which is available for a time t, where t may  .
Thus, with reference to the channel there are 2 ‘degrees of freedom’, i.e. bandwidth or frequency and time.

## Slide 14: Cont…
The signal is characterised by amplitude, frequency, phase and time.

## Slide 15: Cont…
Various multiplexing methods are possible in terms of the channel bandwidth and time, and the signal, in particular the frequency, phase or time. The two basic methods are:
1. Frequency Division Multiplexing (FDM)
When the carrier is frequency, FDM is used.
FDM is an analog technology.
FDM divides the spectrum or carrier bandwidth in logical channels and allocates one user to each channel.
Each user can use the channel frequency independently and has exclusive access of it.
All channels are divided in such a way that they do not overlap with each other.
Channels are separated by guard bands. Guard band is a frequency which is not used by either channel.

## Slide 16: Cont…

## Slide 17: Cont…
2. Time Division Multiplexing (TDM)
TDM is applied primarily on digital signals but can be applied on analog signals as well.
In TDM the shared channel is divided among its user by means of time slot. Each user can transmit data within the provided time slot only.
Digital signals are divided in frames, equivalent to time slot i.e. frame of an optimal size which can be transmitted in given time slot.
TDM works in synchronized mode. Both ends, i.e. Multiplexer and De-multiplexer are timely synchronized and both switch to next channel simultaneously.

## Slide 18: Cont…

## Slide 19: 6.3 Introduction to Ethernet & Wireless Networks
Ethernet is a predominant LAN technology in the world.
Internet Engineering Task Force (IETF) maintains the functional protocols and services for the TCP/IP protocol suite in the upper layers.
However, the functional protocols and services at the OSI Data Link layer and Physical layer are described by various engineering organizations (IEEE, ANSI, ITU) or by private companies (proprietary protocols).
The foundation for Ethernet technology was first established in 1970 with a program called Alohanet.
Alohanet was a digital radio network designed to transmit information over a shared radio frequency between the Hawaiian Islands

## Slide 20: Cont…
Alohanet required all stations to follow a protocol in which an unacknowledged transmission required re-transmitting after a short period of waiting
The techniques for using a shared medium in this way were later applied to wired technology in the form of Ethernet
The first version of Ethernet incorporated a media access method known as Carrier Sense Multiple Access with Collision Detection (CSMA/CD).
CSMA/CD is a type of contention protocol that defines how to respond when a collision is detected, or when two devices attempt to transmit packages simultaneously.
CSMA/CD managed the problems that result when multiple devices attempt to communicate over a shared physical medium.

## Slide 21: Cont…
Characteristics of Ethernet in its early years
The first versions of Ethernet used coaxial cable to connect computers in a bus topology. Each computer was directly connected to the backbone.
These early versions of Ethernet were known as:
Thicknet(10BASE5): cabling distances of up to 500 meters before the signal required a repeater
Thinnet(10BASE2): was smaller in diameter and more flexible than Thicknet and allowed for cabling distances of 185 meters.
The evolved once are:
  cable(coaxial-to-UTP)
  Media Access(CSMA-to-CSMA/CD )
  Physical Topology(Bus-to-Star)

## Slide 22: Cont…
Ethernet Beyond the LAN:
The increased cabling distances enabled by the use of fiber-optic cable in Ethernet-based networks has resulted in a blurring of the distinction between LANs and WANs.
Ethernet was initially limited to LAN cable systems within single buildings, and then extended to between buildings.
It can now be applied across a city in what is known as a Metropolitan Area Network (MAN)

## Slide 23: Cont…
Physical and Data Link Features of Ethernet:
Standards and Implementation
  In 1985, the Institute of Electrical and Electronics Engineers (IEEE) standards committee for Local and Metropolitan Networks published standards for LANs. These standards start with the number 802. The standard for Ethernet is 802.3.

## Slide 24: Cont…
Physical and Data Link Features of Ethernet:
Standards and Implementation
Ethernet operates in the lower two layers of the OSI model (L1 & L2)
Ethernet L1 performs a key role in the communication that takes place between devices, but each of its functions has limitations.
Ethernet at Layer 2 addresses these limitations

## Slide 25: Cont…
Physical and Data Link Features of Ethernet:
Logical Link Control-Connecting to upper layers
Ethernet separates the functions of the Data Link layer into two distinct sub-layers: the Logical Link Control (LLC) sub-layer and the Media Access Control (MAC) sub-layer
The use of these sub-layers contributes significantly to compatibility between diverse end devices
LLC is implemented in software, and its implementation is independent of the physical equipment
In a computer, the LLC can be considered the driver software for the Network Interface Card (NIC). The NIC driver is a program that interacts directly with the hardware on the NIC to pass the data between the media and the Media Access Control sub-layer
The IEEE 802.2 standard
describes the
LLC sub-layer functions

## Slide 26: Cont…
Physical and Data Link Features of Ethernet:
MAC-Getting Data to the Media
MAC is the lower Ethernet sublayer of L2. MAC is implemented by hardware, typically in the computer Network Interface Card (NIC).
The Ethernet MAC sublayer has two primary responsibilities:
  Data Encapsulation
  Media Access Control

## Slide 27: Cont…
Physical and Data Link Features of Ethernet:
Physical Implementation of Ethernet:
Ethernet specifies and implements encoding and decoding schemes that enable frame bits to be carried as signals across the media.
Ethernet devices make use of a broad range of cable and connector specifications
UTP copper cables and optical fiber to interconnect network devices via intermediary devices such as hubs and switches. With all of the various media types that Ethernet supports
The introduction of Gigabit Ethernet has extended the original LAN technology to distances that make Ethernet a MAN and WAN standard.
Today, the same protocol that transported data at 3 Mbps can carry data at 10 Gbps
The success of Ethernet is due to the following factors:
  Simplicity and ease of maintenance
  Ability to incorporate new technologies
  Reliability
  Low cost of installation and upgrade

## Slide 28
  Ethernet
MAC in Ethernet: Functions & Characteristics
Ethernet uses CSMA/CD to detect and handle collisions and manage the resumption of communications
The Process:
Carrier Sense: Listen before transmitting
  If a device detects a signal from another device, it will wait for a specified amount of time before attempting to transmit.
Multi-access :several Ethernet nodes can monitor traffic, or access the media, simultaneously.
Collision Detection: refers to the way nodes respond to a collision
Jam Signal and Random Backoff
  This jamming signal is used to notify the other devices of a collision, so that they will invoke a backoff algorithm
  Backoff algorithm causes all devices to stop transmitting for a random amount of time, which allows the collision signals to subside
  After the delay has expired on a device, the device goes back into the "listening before transmit" mode
Notes: Ethernet uses Carrier Sense Multiple Access with Collision Detection (CSMA/CD) to detect and handle collisions and manage the resumption of communications.
Because all computers using Ethernet send their messages on the same media, a distributed coordination scheme (CSMA) is used to detect the electrical activity on the cable. A device can then determine when it can transmit. When a device detects that no other computer is sending a frame, or carrier signal, the device will transmit, if it has something to send.
The Process:
Carrier Sense
In the CSMA/CD access method, all network devices that have messages to send must listen before transmitting.
If a device detects a signal from another device, it will wait for a specified amount of time before attempting to transmit.
When there is no traffic detected, a device will transmit its message. While this transmission is occurring, the device continues to listen for traffic or collisions on the LAN. After the message is sent, the device returns to its default listening mode.
Multi-access
If the distance between devices is such that the latency of one device's signals means that signals are not detected by a second device, the second device may start to transmit, too. The media now has two devices transmitting their signals at the same time. Their messages will propagate across the media until they encounter each other. At that point, the signals mix and the message is destroyed. Although the messages are corrupted, the jumble of remaining signals continues to propagate across the media.
Collision Detection
When a device is in listening mode, it can detect when a collision occurs on the shared media. The detection of a collision is made possible because all devices can detect an increase in the amplitude of the signal above the normal level.
Once a collision occurs, the other devices in listening mode - as well as all the transmitting devices - will detect the increase in the signal amplitude. Once detected, every device transmitting will continue to transmit to ensure that all devices on the network detect the collision.
Jam Signal and Random Backoff
Once the collision is detected by the transmitting devices, they send out a jamming signal. This jamming signal is used to notify the other devices of a collision, so that they will invoke a backoff algorithm. This backoff algorithm causes all devices to stop transmitting for a random amount of time, which allows the collision signals to subside.
After the delay has expired on a device, the device goes back into the "listening before transmit" mode. A random backoff period ensures that the devices that were involved in the collision do not try to send their traffic again at the same time, which would cause the whole process to repeat. But, this also means that a third device may transmit before either of the two involved in the original collision have a chance to re-transmit.

## Slide 29: CSMA/CD process

## Slide 30
  Ethernet
Ethernet Physical Layer: 10/100/1000Mbps & Future Options
The differences between standard Ethernet, Fast Ethernet, Gigabit Ethernet, and 10 Gigabit Ethernet occur at the Physical layer
Currently Four data rates are defined by IEEE 802.3 for operation over optical fiber and twisted-pair cables:
  10 Mbps - 10Base-T Ethernet
  100 Mbps - Fast Ethernet
  1000 Mbps - Gigabit Ethernet
  10 Gbps - 10 Gigabit Ethernet

## Slide 31
  Ethernet
Ethernet Physical Layer: 10/100/1000Mbps & Future Options

## Slide 32: Wireless Network
What is a wireless network?
  A technology that enables two or more entities to communicate without network cabling
Any application currently used on a traditional wired network can be used on a wireless network.
New applications may be available or can be developed to take advantage of wireless, such as Wireless PDA access to a card catalog.
Why Wireless
Mobility: Wireless LAN systems can provide LAN users with access to real-time information anywhere in their organization. This mobility supports productivity and service opportunities not possible with wired networks.

## Slide 33: Why Wireless?
Installation Speed and Simplicity: Installing a wireless LAN system can be fast and easy and can eliminate the need to pull cable through walls and ceilings.
Reduced Cost-of-Ownership: While the initial investment required for wireless LAN hardware can be higher than the cost of wired LAN hardware, overall installation expenses and life-cycle costs can be significantly lower.
Scalability: Wireless LAN systems can be configured in a variety of topologies to meet the needs of specific applications and installations. Configurations are easily changed and range from peer-to-peer networks suitable for a small number of users to full infrastructure networks of thousands of users that enable roaming over a broad area.

## Slide 34
  Wireless Networks
Comparing WLAN to a LAN:
WLANs connect clients to the network through a wireless access point (AP) instead of an Ethernet switch.
WLANs connect mobile devices that are often battery powered, as opposed to plugged-in LAN devices. Wireless network interface cards (NICs) tend to reduce the battery life of a mobile device.
WLANs support hosts that contend for access on the RF media (frequency bands). 802.11 prescribes collision-avoidance instead of collision-detection for media access to proactively avoid collisions within the media.
WLANs use a different frame format than wired Ethernet LANs. WLANs require additional information in the Layer 2 header of the frame.
WLANs raise more privacy issues because radio frequencies can reach outside the facility.
Notes: WLANs use radio frequencies (RF) instead of cables at the physical layer and MAC sub-layer of the data link layer.
In comparison to cable, RF has the following characteristics:
RF does, such as the limits of a wire in a sheath. The lack of such a boundary allows data frames traveling over the RF media to be available to anynot have boundariesone that can receive the RF signal.
RF is unprotected from outside signals, whereas cable is in an insulating sheath. Radios operating independently in the same geographic area but using the same or a similar RF can interfere with each other.
RF transmission is subject to the same challenges inherent in any wave-based technology, such as consumer radio. For example, as you get further away from the source, you may hear stations playing over each other or hear static in the transmission. Eventually you may lose the signal all together. Wired LANs have cables that are of an appropriate length to maintain signal strength.
RF bands are regulated differently in various countries. The use of WLANs is subject to additional regulations and sets of standards that are not applied to wired LANs.

## Slide 36
  Wireless Networks
WLAN Standards: the 802.11 wireless standards
802.11 wireless LAN is an IEEE standard that defines how radio frequency (RF) in the unlicensed industrial, scientific, and medical (ISM) frequency bands is used for the physical layer and the MAC sub-layer of wireless links
When 802.11 was first released, it prescribed 1 - 2 Mb/s data rates in the 2.4 GHz band. At that time, wired LANs were operating at 10 Mb/s so the new wireless technology was not enthusiastically adopted
Since then, wireless LAN standards have continuously improved with the release of IEEE 802.11a, IEEE 802.11b, IEEE 802.11g, and draft 802.11n.
802.11 -- applies to wireless LANs and provides 1 or 2 Mbps transmission in the 2.4 GHz band.
802.11a -- an extension to 802.11 that applies to wireless LANs and provides up to 54 Mbps in the 5GHz band.
802.11b (also referred to as 802.11 High Rate or Wi-Fi) -- an extension to 802.11 that applies to wireless LANS and provides 11 Mbps transmission (with a fallback to 5.5, 2 and 1 Mbps) in the 2.4 GHz band.
802.11g -- applies to wireless LANs and provides 20+ Mbps in the 2.4 GHz band.
Notes: 802.11a
The IEEE 802.11a adopted the OFDM modulation technique and uses the 5 GHz band.
802.11a devices operating in the 5 GHz band are less likely to experience interference than devices that operate in the 2.4 GHz band because there are fewer consumer devices that use the 5 GHz band. Also, higher frequencies allow for the use of smaller antennas.
There are some important disadvantages to using the 5 GHz band. The first is that higher frequency radio waves are more easily absorbed by obstacles such as walls, making 802.11a susceptible to poor performance due to obstructions. The second is that this higher frequency band has slightly poorer range than either 802.11b or g. Also, some countries, including Russia, do not permit the use of the 5 GHz band, which may continue to curtail its deployment.
802.11b and 802.11g
802.11b specified data rates of 1, 2, 5.5, and 11 Mb/s in the 2.4 GHz ISM band using DSSS. 802.11g achieves higher data rates in that band by using the OFDM modulation technique. IEEE 802.11g also specifies the use of DSSS for backward compatibility with IEEE 802.11b systems. DSSS data rates of 1, 2, 5.5, and 11 Mb/s are supported, as are OFDM data rates of 6, 9, 12, 18, 24, 48, and 54 Mb/s.
There are advantages to using the 2.4 GHz band. Devices in the 2.4 GHz band will have better range than those in the 5GHz band. Also, transmissions in this band are not as easily obstructed as 802.11a.
There is one important disadvantage to using the 2.4 GHz band. Many consumer devices also use the 2.4 GHz band and cause 802.11b and g devices to be prone to interference.
802.11n
The IEEE 802.11n draft standard is intended to improve WLAN data rates and range without requiring additional power or RF band allocation. 802.11n uses multiple radios and antennae at endpoints, each broadcasting on the same frequency to establish multiple streams. The multiple input/multiple output (MIMO) technology splits a high data-rate stream into multiple lower rate streams and broadcasts them simultaneously over the available radios and antennae. This allows for a theoretical maximum data rate of 248 Mb/s using two streams.
The standard is expected to be ratified by September 2008.
Important: RF bands are allocated by the International Telecommunications Union-Radio communication sector (ITU-R). The ITU-R designates the 900 MHz, 2.4 GHz, and 5 GHz frequency bands as unlicensed for ISM communities. Although the ISM bands are globally unlicensed, they are still subject to local regulations. The use of these bands is administered by the FCC in the United States and by the ETSI in Europe. These issues will impact your selection of wireless components in a wireless implementation.

## Slide 37: Wireless Network Components
Access Points
NICs – Network Interface Cards
  PCMCIA(Personal Computer Memory Card International Association)
  USB
  PCI(Peripheral Component Interconnect)
  CompactFlash
Other Wireless Devices
  Bridges and Routers
  Print Servers
PCs, Laptops, PDAs

## Slide 38
Wireless(802.11) Infrastructure Components:
Access Point: connects wireless clients (or stations) to the wired LAN.
an access point converts the TCP/IP data packets from their 802.11 frame encapsulation format in the air to the 802.3 Ethernet frame format on the wired Ethernet network.
An access point is a Layer 2 device that functions like an 802.3 Ethernet hub.
RF is a shared medium and access points hear all radio traffic. Just as with 802.3 Ethernet, the devices that want to use the medium contend for it. Unlike Ethernet NICs, though, it is expensive to make wireless NICs that can transmit and receive at the same time,
so radio devices do not detect collisions. Instead, WLAN devices are designed to avoid them.
Notes: RF signals attenuate. That means that they lose their energy as they move away from their point of origin. Think about driving out of range of a radio station. This signal attenuation can be a problem in a WLAN where stations contend for the medium.
Imagine two client stations that both connect to the access point, but are at opposite sides of its reach. If they are at the maximum range to reach the access point, they will not be able to reach each other. So neither of those stations sense the other on the medium, and they may end up transmitting simultaneously. This is known as the hidden node (or station) problem.
One means of resolving the hidden node problem is a CSMA/CA feature called request to send/clear to send (RTS/CTS). RTS/CTS was developed to allow a negotiation between a client and an access point. When RTS/CTS is enabled in a network, access points allocate the medium to the requesting station for as long as is required to complete the transmission. When the transmission is complete, other stations can request the channel in a similar fashion. Otherwise, normal collision avoidance function is resumed.

## Slide 39
Access points oversee a distributed coordination function (DCF) called Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA).
This simply means that devices on a WLAN must sense the medium for energy (RF stimulation above a certain threshold) and wait until the medium is free before sending.
Because all devices are required to do this, the function of coordinating access to the medium is distributed.
If an access point receives data from a client station, it sends an acknowledgement to the client that the data has been received.
This acknowledgement keeps the client from assuming that a collision occurred and prevents a data retransmission by the client.

## Slide 40: Wireless Operating Mode
The IEEE 802.11 standards specify two operating modes: infrastructure mode and ad hoc mode.
Infrastructure mode is used to connect computers with wireless network adapters, also known as wireless clients, to an existing wired network with the help from wireless router or access point.
Ad hoc mode is used to connect wireless clients directly together, without the need for a wireless router or access point. An ad hoc network consists of up to 9 wireless clients, which send their data directly to each other.

## Slide 41
  Wireless Networks
Wireless Operations : 802.11 Topologies
Wireless LANs can accommodate various network topologies. When describing these topologies, the fundamental building block of the IEEE 802.11 WLAN architecture is the basic service set (BSS). The standard defines a BSS as a group of stations that communicate with each other.
Ad hoc Networks
  Wireless networks can operate without access points; this is called an ad hoc topology. Client stations which are configured to operate in ad hoc mode configure the wireless parameters between themselves. The IEEE 802.11 standard refers to an ad hoc network as an independent BSS (IBSS).

## Slide 42
  Wireless Networks
Wireless Operations: 802.11 Topologies
Basic Service Sets
Access points provide an infrastructure that adds services and improves the range for clients. A single access point in infrastructure mode manages the wireless parameters and the topology is simply a BSS. The coverage area for both an IBSS and a BSS is the basic service area (BSA).

## Slide 43
  Wireless Networks
Wireless Operations: 802.11 Topologies
Extended Service Sets
When a single BSS provides insufficient RF coverage, one or more can be joined through a common distribution system into an extended service set (ESS). In an ESS, one BSS is differentiated from another by the BSS identifier (BSSID), which is the MAC address of the access point serving the BSS. The coverage area is the extended service area (ESA).

## Slide 44
  Wireless Networks
Wireless Operations: 802.11 Topologies
Notes: Common Distribution System
The common distribution system allows multiple access points in an ESS to appear to be a single BSS. An ESS generally includes a common SSID to allow a user to roam from access point to access point.
Cells represent the coverage area provided by a single channel. An ESS should have 10 to 15 percent overlap between cells in an extended service area. With a 15 percent overlap between cells, an SSID, and non-overlapping channels (one cell on channel 1 and the other on channel 6), roaming capability can be created.
Click the Summary button in the figure to see a comparions of WLAN topologies.