## Slide 1
Wollo University
Kombolcha Institute of Technology
Department of Information System
Data Communication and Computer Networks

## Slide 2
    3.1 Network Components
    Hardware
    Software
chapter 03
Components of the network
Notes: The path that a message takes from source to destination can be as simple as a single cable connecting one computer to another or as complex as a network that literally spans the globe. This network infrastructure is the platform that supports our human network. It provides the stable and reliable channel over which our communications can occur.
Devices and media are the physical elements or hardware of the network. Hardware is often the visible components of the network platform such as a laptop, a PC, a switch, or the cabling used to connect the devices. Occasionally, some components may not be so visible. In the case of wireless media, messages are transmitted through the air using invisible radio frequency or infrared waves.
Services and processes are the communication programs, called software, that run on the networked devices. A network service provides information in response to a request. Services include many of the common network applications people use every day, like e-mail hosting services and web hosting services. Processes provide the functionality that directs and moves the messages through the network. Processes are less obvious to us but are critical to the operation of networks.
2

## Slide 3
Components of the network
Network infrastructure is the platform that supports the human network.
  Provides the stable and reliable channel over which communications can occur
As a component Data Network consists Devices, Media & Services
  Devices and media are the physical elements or hardware of the network
  Services and processes are the communication programs, called software, that run on the networked devices
Service provides information in response to a request
  network applications like e-mail hosting services and web hosting services
Processes provide the functionality that directs and moves the messages through the network
Notes: Devices and media are the physical elements or hardware of the network. Hardware is often the visible components of the network platform such as a laptop, a PC, a switch, or the cabling used to connect the devices. Occasionally, some components may not be so visible. In the case of wireless media, messages are transmitted through the air using invisible radio frequency or infrared waves.
Services and processes are the communication programs, called software, that run on the networked devices. A network service provides information in response to a request. Services include many of the common network applications people use every day, like e-mail hosting services and web hosting services. Processes provide the functionality that directs and moves the messages through the network. Processes are less obvious to us but are critical to the operation of networks.
3

## Slide 4
End Devices and their Role in the Network
  End devices form interface with human network & communications network
  Example of end devices…
Role of end devices:
  end devices are referred to as hosts, and can act as:
  Client
  Server
  Both client and server
Components of the network
Notes: The network devices that people are most familiar with are called end devices. These devices form the interface between the human network and the underlying communication network. Some examples of end devices are:
  Computers (work stations, laptops, file servers, web servers)
  Network printers
  VoIP phones
  Security cameras
  Mobile handheld devices (such as wireless barcode scanners, PDAs)
In the context of a network, end devices are referred to as hosts. A host device is either the source or destination of a message transmitted over the network. In order to distinguish one host from another, each host on a network is identified by an address. When a host initiates communication, it uses the address of the destination host to specify where the message should be sent.
A host can act as a client, a server, or both. Software installed on the host determines which role it plays on the network.
Servers are hosts that have software installed that enables them to provide information and services, like e-mail or web pages, to other hosts on the network.
Clients are hosts that have software installed that enables them to request and display the information obtained from the server.
4

## Slide 5
End Devices and their Role in the Network
  Example of end devices
      Computers (work stations, laptops, file servers, web servers)
      Network printers
      VoIP phones
      Security cameras
      Mobile handheld devices (wireless barcode scanners, PDAs)
Software installed on the host determines which role it plays
Servers are hosts that have software installed that enables them to provide information and services, like e-mail or web pages, to other hosts on the network.
Clients are hosts that have software installed that enables them to request and display the information obtained from the server.
Components of the network

## Slide 6
  Intermediary device & their role
  Provides connectivity and ensures data flows across network
  Networks rely on intermediary devices to provide connectivity
Components of the network
Notes: Networks rely on intermediary devices to provide connectivity and to work behind the scenes to ensure that data flows across the network. These devices connect the individual hosts to the network and can connect multiple individual networks to form an internetwork.
6

## Slide 7
Intermediary device & their role
  Example of intermediary devices:
  Network Access Devices (Hubs, switches, and wireless access points)
  Internetworking Devices (Routers)
  Communication Servers and Modems
  Security Devices (firewalls, IDS(Intrusion Detection System), IPS(Intrusion Prevention Systems))
Functions
  Regenerate and retransmit data signals
  Maintain information about what pathways exist
  Notify other devices of errors and communication failures
  Direct data along alternate pathways when there is a link failure
  Classify and direct messages according to QoS priorities
  Permit or deny the flow of data, based on security settings
Components of the network
Notes: Examples:
  Network Access Devices (Hubs, switches, and wireless access points)
  Internetworking Devices (routers)
  Communication Servers and Modems
  Security Devices (firewalls)
The management of data as it flows through the network is also a role of the intermediary devices. These devices use the destination host address, in conjunction with information about the network interconnections, to determine the path that messages should take through the network. Processes running on the intermediary network devices perform these functions:
  Regenerate and retransmit data signals
  Maintain information about what pathways exist through the network and internetwork
  Notify other devices of errors and communication failures
  Direct data along alternate pathways when there is a link failure
  Classify and direct messages according to QoS priorities
  Permit or deny the flow of data, based on security settings
7

## Slide 8: 3.2 Network Types
Network Criteria
Performance: can be measured using
  Transit time - amount of time required for a message to travel)
  Response time - elapsed time between an inquiry and the response
Reliability: measured by the frequency of failure, the time it takes a link to recover from failure, and the network’s robustness in a catastrophe
Security: protecting data and network infrastructure from unauthorized access

## Slide 9
Local Area Network(LAN)
Networks infrastructures can vary greatly in terms of:
  The size of the area covered
  The number of users connected
  The number and types of services available
An individual network usually spans a single geographical area, providing services and applications to people within a common organizational structure, such as a single business, campus or region.
This type of network is called a Local Area Network (LAN).
A LAN is usually administered by a single organization.
The administrative control that governs the security and access control policies are enforced on the network level.

## Slide 10: Metropolitan Area Network
A metropolitan area network (MAN) is a computer network that usually spans a city or a large campus.
A MAN usually interconnects a number of local area networks (LANs) using a high-capacity backbone technology, such as fiber-optical links, and provides up-link services to wide area networks(or WAN) and the Internet.
A MAN is optimized for a larger geographical area than a LAN, ranging from several blocks of buildings to entire cities.
MANs can also depend on communications channels of moderate-to-high data rates.
A MAN might be owned and operated by a single organization, but it usually will be used by many individuals and organizations.
MANs might also be owned and operated as public utilities.
They will often provide means for internetworking of local networks

## Slide 11: Wide Area Network
When a company or organization has locations that are separated by large geographical distances, it may be necessary to use a telecommunications service provider (TSP) to interconnect the LANs at the different locations.
Telecommunications service providers operate large regional networks that can span long distances.
Traditionally, TSPs transported voice and data communications on separate networks.
Increasingly, these providers are offering converged information network services to their subscribers.
Individual organizations usually lease connections through a telecommunications service provider network.
These networks that connect LANs in geographically separated locations are referred to as Wide Area Networks (WANs).

## Slide 12: WAN(cont…)
Although the organization maintains all of the policies and administration of the LANs at both ends of the connection, the policies within the communications service provider network are controlled by the TSP.
WANs use specifically designed network devices to make the interconnections between LANs.
Because of the importance of these devices to the network, configuring, installing and maintaining these devices are skills that are integral to the function of an organization's network.
LANs and WANs are very useful to individual organizations. They connect the users within the organization.
They allow many forms of communication including exchange e-mails, corporate training, and other resource sharing.

## Slide 13: Internet: A network of Networks
Although there are benefits to using a LAN or WAN, most of us need to communicate with a resource on another network, outside of our local organization.
Examples of this type of communication include:
  Sending an e-mail to a friend in another country
  Accessing news or products on a website
  Getting a file from a neighbor's computer
  Instant messaging with a relative in another city
  Following a favorite sporting team's performance on a cell phone
Internetwork
A global mesh of interconnected networks (internetworks) meets these human communication needs.
Some of these interconnected networks are owned by large public and private organizations, such as government agencies or industrial enterprises, and are reserved for their exclusive use.

## Slide 14: Internet(cont…)
The most well-known and widely used publicly-accessible internetwork is the Internet.
The Internet is created by the interconnection of networks belonging to Internet Service Providers (ISPs).
These ISP networks connect to each other to provide access for millions of users all over the world.
Ensuring effective communication across this diverse infrastructure requires the application of consistent and commonly recognized technologies and protocols as well as the cooperation of many network administration agencies.
Intranet
The term intranet is often used to refer to a private connection of LANs and WANs that belongs to an organization, and is designed to be accessible only by the organization's members, employees, or others with authorization.

## Slide 15: Internet(cont…)
Extranet is part of an Intranet, which is also categorized as a “Private Network”.
It is controlled and managed by an organization, to provide secure access to Intranet from the outside world.
Many business organizations need their business partners and customers to connect to Intranet to enhance communication and efficiency.
Since the Intranet permits only internal members to gain access, external members (partners and customers) use Extranet to access the network
system administration/management can decide which users should allow through Extranet. Generally, external users are given limited access over the Intranet.
Not only external users, sometimes members of the organization itself who may need to access the network over the Internet can use Extranet.

## Slide 16
Note: The following terms may be interchangeable: internetwork, data network, and network.
A connection of two or more data networks forms an internetwork - a network of networks.
It is also common to refer to an internetwork as a data network - or simply as a network - when considering communications at a high level. The usage of terms depends on the context at the time and terms may often be interchanged.

## Slide 17: Network Application Architecture
Application architecture is designed by the application developer and dictates how the application is structured over the various end systems.
When choosing the developer can choose among the two predominant architectural paradigms used in modern network application.
    Client server architecture and
    Peer to peer architecture
    Hybrid of client-server and P2P

## Slide 18: Client-server architecture
server:
  always-on host
  permanent IP address
  server farms for scaling
clients:
  communicate with server
  may b intermittently connected
  may have dynamic IP addresses
  do not communicate directly with each other
client/server

## Slide 19: Cont…
Fig. One of Google data center
Often in client server application, a single host server is incapable of keeping up with all the request from its clients.
For example Facebook or Google will quickly be overwhelmed if it has only one server handling all of its requests.
For this reason, a large cluster of hosts- some times referred as data centers are often used to create a powerful virtual server.

## Slide 20: Pure P2P architecture
no always-on server
arbitrary end systems directly communicate
peers are intermittently connected and change IP addresses
They are not owned by internet service providers
They are simple desktop, laptop controlled by users
Highly scalable but difficult to manage
Peer to peer application examples
  Emule , bit torrent, internet telephony
peer-peer

## Slide 21: Hybrid of client-server and P2P
Skype
  voice-over-IP P2P application
  centralized server: finding address of remote party:
  client-client connection: direct (not through server)
Instant messaging
  chatting between two users is P2P
  centralized service: client presence detection/location
    user registers its IP address with central server when it comes online
    user contacts central server to find IP addresses of buddies

## Slide 22: Network Topologies
What is a Topology?
The term topology, or more specifically, network topology, refers to the arrangement or physical layout of computers, cables, and other components on the network. "Topology" is the standard term that most network professionals use when they refer to the network's basic design.
Topology describes how the network is constructed.

## Slide 23: A network's topology affects its capabilities. The choice of one topology over another will have an impact on the:
  Type of equipment the network needs.
  Capabilities of the equipment.
  Growth of the network.
  Way the network is managed.

## Slide 24: Types of topologies
Linear Bus Topology
Star Topology
Ring Topology
Mesh Topolgy
By modifying and combining some of the characteristics of these “pure” network topologies , “hybrid” topologies result that can often provide greater efficiency.
eg. Tree, star-star, hybrid topology.

## Slide 25: 1. Linear Bus (Bus)
A linear bus topology consists of a main run of cable with a terminator at each end (See fig.All nodes (file server, workstations, and peripherals) are connected to the linear cable.

## Slide 26: Advantages of a Linear Bus Topology
Easy to connect a computer or peripheral to a linear bus.
Requires less cable length than a star topology.
Very easy to extend

## Slide 27: Disadvantages of a Linear Bus Topology
Entire network shuts down if there is a break in the main cable.
Terminators are required at both ends of the backbone cable.
Difficult to identify the problem if the entire network shuts down.
The trunk can be bottle neck to the network when network traffic is very heavy.

## Slide 28: 2. Star
A star topology is designed with each node (file server, workstations, and peripherals) connected directly to a central network hub or Switch.
Data on a star network passes through the hub before continuing to its destination.

## Slide 29: Advantages of a Star Topology
Easy to install and wire.
No disruptions to the network then connecting or removing devices.
Easy to detect faults and to remove parts.

## Slide 30: Disadvantages of a Star Topology
Requires more cable length than a linear topology.
If the hub or fails, nodes attached are disabled.
More expensive than linear bus topologies because of the cost of the hubs and cable.

## Slide 31: 3. Ring Topology
The ring topology connects computers on a single circle of cable.
Unlike the bus topology, there are no terminated ends. The signals travel around the loop in one direction and pass through each computer, which can act as a repeater to boost the signal and send it on to the next computer.
The failure of one computer can have an impact on the entire network.
A star-wired ring topology may appear (physically) to be the same as a star topology. Logically, the MAU (multistation access unit) of a star-wired ring contains wiring that allows information to pass from one device to another in a circle or ring.

## Slide 32: Ring topology

## Slide 33: Token Passing
One method of transmitting data around a ring is called token passing. (A token is a special series of bits that travels around a token-ring network. Each network has only one token.)
The token is passed from computer to computer until it gets to a computer that has data to send.
The sending computer modifies the token, puts an electronic address on the data, and sends it around the ring.

## Slide 34: Advantages of a Ring Topology
Fault diagnostic and isolation are relatively easy
The modular design results in a network that is easy to expand

## Slide 35: Disadvantages of a Ring Topology
Network configuration can be technically complicated
The cabling system is complicated

## Slide 36: 4. Mesh Topology
A mesh topology network offers superior redundancy and reliability.
In a mesh topology, each computer is connected to every other computer by separate cabling. This configuration provides redundant paths throughout the network so that if one cable fails, another will take over the traffic.
While ease of troubleshooting and increased reliability are definite things, these networks are expensive to install because they use a lot of cabling.

## Slide 37: Mesh topology

## Slide 38: 5.Hybrid Topologies
5.1 Star Bus
The star bus is a combination of the bus and star topologies.
In a star-bus topology, several star topology networks are linked together with linear bus trunks.
If one computer goes down, it will not affect the rest of the network.
The other computers can continue to communicate. If a hub goes down, all computers on that hub are unable to communicate. If a hub is linked to other hubs, those connections will be broken as well.

## Slide 39: 5.2 Star Bus

## Slide 40: 5.3 Star Ring
The star ring (sometimes called a star-wired ring) appears similar to the star bus. Both the star ring and the star bus are centered in a hub that contains the actual ring or bus.
Linear-bus trunks connect the hubs in a star bus, while the hubs in a star ring are connected in a star pattern by the main hub.

## Slide 41: Star Ring

## Slide 42: 5.3 Tree
A tree topology combines characteristics of linear bus and star topologies.
It consists of groups of star-configured workstations connected to a linear bus backbone cable .
Tree topologies allow for the expansion of an existing network, and enable organizations to configure a network to meet their needs.

## Slide 44
Advantages of a Tree Topology
Point-to-point wiring for individual segments.
Supported by several hardware and software venders.
Disadvantages of a Tree Topology
Overall length of each segment is limited by the type of cabling used.
If the backbone line breaks, the entire segment goes down.
More difficult to configure and wire than other topologies.

## Slide 45: Summary
Topology | Advantages | Disadvantages
Bus | Use of cable is economical. Media is inexpensive and easy to work with. System is simple and reliable. Bus is easy to extend. | Network can slow down in heavy traffic. Problems are difficult to isolate. Cable break can affect many users.
Ring | System provides equal access for all computers. | Failure of one computer can impact the rest of the network. Problems are hard to isolate.
Star | Modifying system and adding new computers is easy. Centralized monitoring and management are possible. Failure of one computer does not affect the rest of the network. | If the centralized point fails, the network fails.
Mesh | System provides increased redundancy and reliability as well as ease of troubleshooting. | System is expensive to install because it uses a lot of cabling.

## Slide 46
                CHAPTER END
                ???